## Slide 1: IR/THz Double Resonance Spectroscopy in the Pressure Broadened Regime: A Path Towards Atmospheric Gas Sensing
Sree H. Srikantaiah
Dane J. Phillips
Frank C. De Lucia
Henry O. Everitt

## Slide 2
GHz
Why apply Double Resonance Spectroscopy for Atmospheric sensing ?
Traditional smm/THz spectroscopy has absolute specificity at low pressures due to highly resolved rotational lines - great technique for sensing at low pressures
At atmospheric pressure this specificity and sensitivity is lost due to pressure broadening (5GHz linewidths)
Difficulty due to added problems in detection of molecular resonances due to atmospheric fluctuations
2T
1T
500mT
100mT
Notes: We have discussed point sensors based on Doppler limited SMM spectra.
For Paper XXX at this meeting.
But the linewidths at atmospheric pressure make this much harder
At bottom, briefly note, but do not elaborate on the Specificity and sensitivity points
(this is the introduction to the next chart)

## Slide 3
Double resonance spectroscopy – Example 12CH3F
Spectral and temporal features
Pulsed
CO2 Laser
THz Detector
THz Detector
Gas Cell
Experimental setup
Estimated DR signatures for the 3 IR transition types

## Slide 4: IR/THzDouble Resonance: Strategy for Atmospheric Remote sensing
13CH3F Specificity Matrix
Choose suitable IR pump laser line coincidence.
Match IR pump pulse width to atmospheric relaxation rates (~ 100ps).
Choose appropriate water vapor transmission window for THz beams.
Monitor THz wave modulation initiated by the IR pump laser.
Establish a 3D specificity matrix with as many points as possible – to increase specificity for a particular molecule.
Separation of target signature from atmospheric clutter by locking on to IR pulse sequence/rep frequency.

## Slide 5
Pulsed IR Pump Laser:
Spectral and Temporal Requirements
At low pressures the coincidence requirement is that the laser line be within twice the Doppler width of the molecular transition (i.e within 66MHz for CH3F)
Coincidence requirement at Atmospheric pressures is relaxed due to Pressure broadening ~ 2.3 GHz line width (Δν) (i.e. within 4.6 GHz ) -- more spectral coincidences are now available
The pump intensity must be high enough such that Rabi frequency is comparable to the atmospheric relaxation rate (1/π Δν) ~ 100ps
The laser temporal pulse width should at least be of the order of 100 ps to facilitate the movement of population of the sample molecule at atmospheric relaxation rates

## Slide 6
Pressure Broadening – Increase in spectral coincidences
IR spectral coincidences for CH3 35 Cl increases from 2 at low pressures to more than 300 at atmospheric pressures !!

## Slide 7
Short pulse generation using Optical Free Induction Decay (OFID)
- TEA CO2 laser pulse is typically 50ns wide temporally and ~ 200MHz wide spectrally
- Truncating the pulse using plasma shutter produces a sharp temporal transition as well as widens frequency spectrum
- OFID filter (hot CO2 gas cell) absorbs fundamental frequency only
- Typical temperature of Hot cell = 400oC
- By varying pressure in the hot cell output pulse lengths can be tuned
R. Kesselring, et al., IEEE J. Quant. Elect. 29, 997 (1993).

## Slide 8
Proposed Experiment
TEA CO2 laser
Spectrometer
Plasma shutter
CO2 Hot Cell
High speed IR detector
THz source
THz Heterodyne Reciever
Sample cell
6 GHz , 40 GS/s Digitizing Oscilloscope
Data acquisition
DR signal
Trigger
50ns 30 Hz
0.15 J
~ 100ps
OFID

## Slide 9
Partially self-modelocked
Complete self-modelocked
CO2 TEA laser pulse characteristics

## Slide 10
CO2 TEA laser temporal pulse characteristics
Partially - modelocked pulse profile

## Slide 11
(a)
(c)
(d)
(b)
8T – Max signal
CO2 Laser line = 10R14 (J24,K0 –J24,K0)
636.591 GHz (RO-)
IR Mismatch = 115.727 MHz
Proof of Principle - Experimental Data

## Slide 12
Conclusion and future plans
The scope and principles of DR remote sensing technique were discussed
The technology and hardware required to realize the remote sensing application were discussed
Preliminary proof of principle experimental data has been obtained which supports our idea for application of Double resonance spectroscopy for Remote sensing.
Future plans :
Construction of the 100ps CO2 pump laser system.
Construction of the fast receiver and data acquisition system.
Experimental demonstration of the sensing scheme at elevated pressures and ultimately at atmospheric pressures
Extending the application to detect larger molecules and more important real world threat molecules