10/20/40 Turns (5K10.21)

Location: 29-5R

Concept/Purpose: Induced Currents and Forces

Procedure/Explanation: Three separate copper coils are mounted to a piece of clear plexiglass in parallel with a small built in galvanometer. The coils are 10, 20, and 40 turns respectively so that when a small cow magnet is used to induce current the galvanometer deflection approximately doubles for each successive coil. The entire apparatus fits on an overhead projector for presentation to the class.