Internal Resistance (5E40.75)

Location: 29-1L

Concept/Purpose: Cells and Batteries

Procedure/Explanation: A weak 9V battery is placed in series with a resistor and a switch.  The voltage of the battery is measured while the switch is open; then it is measured while the switch is closed.  The lower voltage measured while the switch is closed is due to the batteries internal resistance.