Piezo Sparker and Scope (5E60.20)

Location: Dick

Concept/Purpose: Piezoelectricity

Procedure/Explanation: A starter (sparker) for a gas grill is connected to an oscilloscope.  When the starter is pressed, a large voltage can be viewed on the oscilloscope.