Variac and Light Bulb (5F20.18)

Location: 29-1R

Concept/Purpose: Electrical resistance/power.

Procedure/Explanation: A long filament, white light bulb is connected to an electronic wattmeter and a variac. The variac is slowly turned up from 0 volts to 120 volts to show that as the voltage is increased the current increases resulting in an increase in power which. The power increase is observed on the wattmeter and also visually by watching the light go from a dull orange glow at the low voltages bright white glow at the higher voltages.